## Slide 1: HPCC 24: Paper 1571072796 HIDC: Heterogeneous-ISA Dynamic Core Nirmal Kumar Boran, Prakhar Diwan, Meet Udeshi, Shubhakit Rathore and Virendra Singh

## Slide 2: Outline
Introduction
Motivation
Proposal
Experimental Setup
Simulation Results
Conclusion
References

## Slide 3: Introduction
Computing is heavily diverging towards:
  Mobile space
  Data center space
Data center space involves multitude of processors integrated in multiple servers, which cater to large compute demands
Mobile space comprises of devices such as tablets, smartphones etc., which cater to lower-compute applications

## Slide 4: Shared aim for mobile & data center compute
Data centers remain major consumers of electrical power[a][b]
  Consumption as high as 416 Terawatt-hours in 2017
  It follows an increasing trend → need for energy-efficiency
Mobile devices are becoming popular as they support ever-increasing range of applications, but:
  they operate on battery → need for energy savings
Hence, both spaces share a common target of energy efficiency
[a] https://www.techtarget.com/searchdatacenter/tip/How-much-energy-do-data-centers-consume
[b]https://cc-techgroup.com/data-center-energy-consumption/#:~:text=Data%20centers%20usually%20use%20a,and%20cool%20down%20their%20components

## Slide 5: Achieving Energy Efficiency
Architects analysed the workloads and observed their diverse needs across and within programs, such as:
  varying ILP vs TLP requirements
  high-ILP vs low-ILP, memory intensive phases
One solution to deal with this diversity→through heterogeneity[1][2]:
  using cores with different performance & power characteristics
  switching phases/applications between such cores, based on optimal matching
  led to significant energy efficiency benefits
[1] R. Kumar et. al, “Single-ISA Heterogeneous Multi-Core Architectures: the potential for processor power reduction”, MICRO 2003
[2] R. Kumar et. al, “Single-ISA Heterogeneous Multi-Core Architectures for Multithreaded Workload Performance”, ISCA 2004

## Slide 6: Heterogeneous Computing
Energy efficiency has been extracted by various heterogeneity dimensions such as:
  Core sizes (issue-widths)
  Execution semantics (in-order/out-of-order)
  Number of cores
Later, ISA was added as a dimension, after Devuyst[3] presented cross-ISA migration techniques for a heterogeneous ISA CMP
Why does ISA have significant potential?
[3] M. Devuyst et. al, “Execution migration in a heterogeneous ISA chip multiprocessor”, ASPLOS 2012
Notes: However it was all restricted to a single ISA

## Slide 7: ISA affinity
[4] A. Venkat et. al, “Harnessing ISA diversity: Design of a heterogeneous-ISA chip multiprocessor”. ISCA, 2014.
ARM affine
Notes: Here I have plotted the execution time of consecutive phases of 100M instructions from bzip2 benchmark.
Dynamic execution of phases on affine ISA led to 24% improvement over best single-ISA execution.

## Slide 8: ISA affinity
[4] A. Venkat et. al, “Harnessing ISA diversity: Design of a heterogeneous-ISA chip multiprocessor”. ISCA, 2014.
x86 affine
Notes: Here I have plotted the execution time of consecutive phases of 100M instructions from bzip2 benchmark.
Dynamic execution of phases on affine ISA led to 24% improvement over best single-ISA execution.

## Slide 9: ISA affinity
[4] A. Venkat et. al, “Harnessing ISA diversity: Design of a heterogeneous-ISA chip multiprocessor”. ISCA, 2014.
24% speedup
Reason for speedup?
Notes: Here I have plotted the execution time of consecutive phases of 100M instructions from bzip2 benchmark.
Dynamic execution of phases on affine ISA led to 24% improvement over best single-ISA execution.

## Slide 10: ISA Diversity
Different ISAs may have different sets of features:
  Architectural register file size
  Types of memory operand support
  Instruction format
  Types of operand support
These affect various performance parameters:
  Register pressure
  Code density
  Dynamic instruction count
[4] A. Venkat et. al, “Harnessing ISA diversity: Design of a heterogeneous-ISA chip multiprocessor”. ISCA, 2014.
Notes: How to implement such a different ISA system and migration between the cores..

## Slide 11: Heterogeneous ISA CMP (HISACMP)
CMP consisting of different ISA cores with private LLCs
Process migrates between the cores dynamically as per affinity
32% reduction in EDP compared to best single-ISA architecture
[4] A. Venkat et. al, “Harnessing ISA diversity: Design of a heterogeneous-ISA chip multiprocessor”. ISCA, 2014.
ISA-1
ISA-2
ISA-3
L1$
L1$
L1$
L2$
L2$
L2$

## Slide 12: Cross-ISA migration techniques
Coarse-grained strategies[3][4][5]:
  Can switch at anytime between ISAs
  Large migration overhead (~100 μs)
Finer-grained strategies[6]:
  Switch at function call & return sites
  Lower migration overhead (~100 ns)
[3] M. Devuyst et. al, “Execution migration in a heterogeneous ISA chip multiprocessor”, ASPLOS 2012
[4] A. Venkat et. al, “Harnessing ISA diversity: Design of a heterogeneous-ISA chip multiprocessor”. ISCA, 2014.
[5] A. Barbalace et. al, “Breaking the Boundaries in Heterogeneous-ISA Datacenter”. ASPLOS, 2017.
[6] N. Boran et. al, “Fine-Grained Scheduling in Heterogeneous-ISA Architectures”, CAL 2021
Notes: – Load balancing – spread workload evenly across available servers
– Consolidation – group workload on minimal number of machines, idle or power down others

## Slide 13: Motivation: Heterogeneous-ISA Execution
ISA-1
ISA-2
L1$
L2$
L1$
L2$
Main Memory
IDLE
ACTIVE
Notes: Single-threaded execution in HISACMP/HISADC

## Slide 14: Motivation: Heterogeneous-ISA Execution
ISA-1
ISA-2
L1$
L2$
L1$
L2$
Main Memory
ACTIVE
IDLE
Notes: Single-threaded execution in HISACMP/HISADC

## Slide 15: Motivation: Heterogeneous-ISA Execution
ISA-1
ISA-2
L1$
L2$
L1$
L2$
Main Memory
IDLE
ACTIVE
Heterogeneous ISA CMP execution involves switching between cores, which leads to:
  Static power dissipation by idle cores
  Core resources are underutilized
Also, migration overhead (~100μs) is large due to separate LLCs
Can we make heterogeneous ISA execution (single-threaded) more energy-efficient?
Notes: Single-threaded execution in HISACMP/HISADC

## Slide 16: Heterogeneous ISA Dynamic Core (HIDC)
HIDC consists of:
  a dynamic out-of-order core supporting multiple ISAs
  migration engine to facilitate cross-ISA migration
Core consists a superset of resources required by the ISAs
It overcomes static power and resource utilization issues
For cross-ISA switching decisions, HIDC uses a perceptron-based scheduler[7]
We use the two popular ISAs ARM & x86 for the proposal
[7] N. Boran et. al, “Classification based scheduling in Heterogeneous ISA Architectures”. VDAT, 2020.
How to execute multiple ISAs within a core?
Notes: How

## Slide 17: HIDC
Notes: Simultaneous transformation is done at L2 level so it’s fast as most recent stack frames are present..

## Slide 18: HIDC Pipeline
CIB: Indicates the executing ISA
Remains unaltered across ARM/x86 execution
Notes: Simultaneous transformation is done at L2 level so it’s fast as most recent stack frames are present..

## Slide 19: HIDC Pipeline
ISA-specific decoders are used
Notes: Instruction blocks are demultiplexed to the appropriate decoder based on the CIB signal

## Slide 20: HIDC Pipeline
Common register files & renaming logic are used by both ISAs
Notes: We append the register bits according to ARM as 5, as it contains 32 architectural registers.

## Slide 21: HIDC Pipeline
RS, ROB, SB entries are modified
to incorporate exclusive ISA information
Notes: SB - store buffer

## Slide 22: HIDC Pipeline
Only x86 uses SIMD
and FP Functional Units
Notes: Simultaneous transformation is done at L2 level so it’s fast as most recent stack frames are present..

## Slide 23: HIDC Pipeline
Common ROB & SB is used
Notes: Simultaneous transformation is done at L2 level so it’s fast as most recent stack frames are present..

## Slide 24: Simultaneous Transformation
Stack
Memory
Growth
Migration
Engine
HIDC Execution
A
B
C
x86 execution: C()
Time
Equivalence point: call D()
X86 Format
ARM Format
Being transformed
Notes: Simultaneous transformation is done at L2 level so it’s fast as most recent stack frames are present..

## Slide 25: Simultaneous Transformation
Stack
Memory
Growth
Migration
Engine
A
B
C
x86 execution: C()
Time
Decide to
migrate
Equivalence point: call D()
X86 Format
ARM Format
Being transformed
HIDC Execution
Notes: Simultaneous transformation is done at L2 level so it’s fast as most recent stack frames are present..

## Slide 26: Simultaneous Transformation
Stack Memory
Growth
Migration
Engine
Transform(A,B)
A
B
C
A
B
C
x86 execution: C()
Time
Decide to
migrate
Equivalence point: call D()
X86 Format
ARM Format
Being transformed
HIDC Execution
Notes: Simultaneous transformation is done at L2 level so it’s fast as most recent stack frames are present..

## Slide 27: Simultaneous Transformation
Stack Memory
Migration
Engine
Idle
Transform(A,B)
A
B
C
A
B
C
A
B
C
x86 execution: C()
Time
Decide to
migrate
Equivalence point: call D()
Migrate to ARM
X86 Format
ARM Format
Being transformed
Transform
(C)
HIDC Execution
Growth
Notes: Simultaneous transformation is done at L2 level so it’s fast as most recent stack frames are present..

## Slide 28: Simultaneous Transformation
Stack Memory
Growth
Migration
Engine
Idle
Transform(A,B)
A
B
C
A
B
C
A
B
C
A
B
C
x86 execution: C()
Time
Decide to
migrate
Equivalence point: call D()
Migrate to ARM
X86 Format
ARM Format
Being transformed
Transform (C)
HIDC Execution
Notes: Simultaneous transformation is done at L2 level so it’s fast as most recent stack frames are present..

## Slide 29: Simultaneous Transformation
Stack
Memory
Growth
Migration
Engine
Idle
Transform(A,B)
A
B
C
A
B
C
A
B
C
A
B
C
x86 execution: C()
ARM execution: D()
Time
Decide to
migrate
Equivalence point: call D()
Migrate to ARM
X86 Format
ARM Format
Being transformed
Transform (C)
HIDC Execution
Notes: Simultaneous transformation is done at L2 level so it’s fast as most recent stack frames are present..

## Slide 30: Simultaneous Transformation
Stack
Memory
Growth
Migration
Engine
Idle
Transform(A,B)
A
B
C
A
B
C
A
B
C
A
B
C
x86 execution: C()
ARM execution: D()
Decide to
migrate
Equivalence point: call D()
Migrate to ARM
X86 Format
ARM Format
Being transformed
Transform (C)
x86 execution
Transform(A,B)+ Transform(C)
ARM execution
Previous Proposal[2]
[2]: A. Venkat et.al, Design of a heterogeneous-ISA chip multiprocessor. ISCA 2014.
HIDC Execution
Notes: Simultaneous transformation is done at L2 level so it’s fast as most recent stack frames are present..

## Slide 31: Experimental Setup: Core Configurations
Configuration | HISACMP |  | HIDC (ARM/X86)
 | ARM core | X86 core | 
4-wide Out-of-Order 3 GHz clock | ROB=108 LQ=16 SQ=16 RS=36 | ROB=192 LQ=36 SQ=48 RS=64 | ROB=192 LQ=36 SQ=48 RS=64
Functional Units | IntALU=4, IntMultDiv=2, FPALU=0/2, FPMultDiv= 0/2, SIMD Units=0/2 |  | 
Performance analysis done using gem5 v20.0 simulator
HISACMP - Heterogeneous ISA CMP (baseline), HIDC - Heterogeneous ISA Dynamic Core (proposal)
Notes: Mention HISACMP is a dual core system with ARM and x86 core each with private LLCs.

## Slide 32: Experimental Setup: Cache Configuration
Performance analysis done using gem5 v20.0 simulator
L1 I-Cache | 32 KB, 8-way, 2 cycle latency | 
L1 D-Cache | 32 KB, 8-way, 2 cycle latency | 
Last Level Cache | 2 MB, 16-way, 15 cycle latency | 
Private LLCs of 2MB were used with ARM and x86 cores in HISACMP
Notes: Private LLCs are used by HISACMP.. And explain that it’s used as baseline.

## Slide 33: ISA Affinity of HIDC
Applications display different affinities towards ARM & x86
Notes: Explain a few cases like: milc uses SIMD functionality available in x86 used byt HIDC and soplex uses FP too.. In ARMv7 it performs that by software emulations.
Mcf is a memory intensive benchmark and effectively utilizes the ARM’s lower register pressure to it’s advantage..

## Slide 34: Migration Overhead
Significant reduction due to Simultaneous Transformation and Shared Cache Hierarchy across different ISA executions
Notes: Reduction due to simultanoues transformation strategy and shared cache across different ISA program execution

## Slide 35: Perceptron based scheduling
On average >90% accuracy was achieved
Notes: Reduction due to simultanoues transformation strategy and shared cache across different ISA program execution

## Slide 36: HIDC Performance
4.62% speedup over HISACMP
19.06% speedup over X86 Core

## Slide 37: HIDC Performance Per Joule
52.89% and 33.93% gain in PPJ over
HISACMP and X86-ISA Core

## Slide 38: Analysis on Multiprogrammed Workloads
50.36% PPJ increase over HISACMP (with power gating)
Notes: Explain the baseline configuration in each dual and quad core config.
Executed 330 quad combinations and 55 pairs from SPEC benchmarks were used.
Explain each metric and gains..

## Slide 39: Conclusion
HIDC achieves 52.89% performance per joule improvements over Heterogeneous ISA CMP on single-threaded applications
Simultaneous Transformation achieves ~20x reduction in cross-ISA migration overheads compared to prior works
HIDC achieves 4.62% performance gains by exploiting finer phases due to lower switching overheads
On MP* workloads, it obtains ~50% performance per joule benefits for a dual-HIDC system; reducing energy consumption by 32%
[*] MP - multi-programmed

## Slide 40: Thank You