## Slide 1: Lichen: Leveraging Coupled Heterogeneity
Prakhar Diwan[a], Nirmal Kumar Boran[b] and Virendra Singh[a]
[a] Indian Institute of Technology Bombay, India
[b] National Institute of Technology Calicut, India
Paper ID: 215

## Slide 2: Introduction
Moore’s law persisted with shrinking transistors, however, Vth reduction plateaued, limiting the number of active transistors
Heterogeneous CMPs effectively trade area for energy efficiency[1]
  Cores with different perf. and power values to meet diverse demands
  Cores vary across dimensions such as InO/OoO, issue-widths etc.
ISA is a recent addition[2] to list of heterogeneity dimensions, due to:
  ISAs have different feature sets (instr format, operand support etc.)
  These impact performance parameters (register pressure, code density etc.)
Notes: that can operate within the power budget.

## Slide 3: Motivation
Heterogeneous-ISA CMPs outperformed single-ISA counterparts over performance and energy efficiency metrics[3]
  However, they utilized oracular scheduling and uniform phases to analyse heterogeneity dimensions in design space exploration
ISA[4] and execution semantics (InO/OoO) [5] have fared better at finer phases, individually
Do these exhibit synergy, when utilized together?
  Let’s analyse program using different ISA cores with different execution modes

## Slide 4: Motivation
Finer switching between ISA cores improves performance

## Slide 5: Motivation
In-order mode utilization increases at finer granularities
Utilize 1M for ISA and 1K for InO/OoO switching
How to schedule such phases?

## Slide 6: Lichen: Overview
Single-ISA Out-of-order Execution
Heterogenous-ISA Out-of-order Execution (1M phase length)
X86-ISA
ARM-ISA
X86-ISA
ARM-ISA
OoO
InO
InO
OoO
OoO
Heterogenous-ISA InO/OoO Execution (1K phase length)

## Slide 7: Using InO/OoO Morphing
An existing facility in modern processors for hardware debug[6]
Further reduction in switching overheads for InO/OoO by morphing:
  Common architecture register file used, avoiding state transfer
On OoO to InO, ROB flushed & instructions re-fetched in InO mode
InO to OoO, ROB is powered on & starts fresh

## Slide 8: Lichen
Heterogeneous CMP with different ISA out-of-order cores morphing into in-order cores based on upcoming program phase
Migration between different-ISA cores[3] and execution modes[6] performed as in prior works
We decouple scheduling problem to 2 levels:
  Predicting affine-ISA core at 1M instruction granularity
  Deciding efficient execution mode at 1K instructions within same-ISA phase
CART decision tree algorithm was found optimal from decision accuracy and number of parameters required for predicting both

## Slide 9: Lichen
Parameter | Purpose
L1-I misses | Stalls due to cache misses
L1-D misses | 
L2-misses | 
ROB full events | Execution pipeline stalls
IQ full events | 
ILP | Parallelism of the executing program
MLP | 
Branch misprediction | Performance Impact of branch predictor
Float instruction count | ISA-specific parameter

## Slide 10: Experimental Setup
OoO/InO Core (ARM & X86) | Superscalar Width=2, 108-entry ROB, 16-entry LQ, 16-entry SQ, 36-entry IQ, 3 GHz Clock, 256 Int PhyReg, 256 FP PhyReg
Functional Units ARM/X86 | IntALU=2, IntMultDiv=1, FPALU=0/1, FPMultDiv= 0/1, SIMD Units=0/1
L1 I-Cache | 32 KB, 8-way, 2 cycle latency
L1 D-Cache | 32 KB, 8-way, 2 cycle latency
Last Level Cache | 2 MB, 16-way, 15 cycle latency
Dual Core System with ARM & X86 simulated using gem5

## Slide 11: Results: ISA/μarch Affinity

## Slide 12: Results: ISA-Scheduling Accuracy

## Slide 13: Results: μarch-Scheduling Accuracy

## Slide 14: Results: Performance

## Slide 15: Results: Energy Consumption

## Slide 16: Conclusion
Lichen uses finer-grained switching between ISAs and existent OoO to InO morphing feature (at runtime), improving energy efficiency
ISA & microarchitectural heterogeneity, leveraged effectively provides significant energy benefits with synergy in interaction
Lichen achieves 15.36% energy savings with 9.36 % EDP reduction over HISACMP (oracular scheduling), with 6.35% performance loss
CART-based scheduling achieves 85.44% and 91.35% accuracy for predicting optimal ISA and execution scheme (InO/OoO)

## Slide 17: Thank You